## Slide 1: Integrating Professional River Study Techniques into School Fieldwork
Project 1:
Comparative Study of River Regimes
Notes: Images:
- (left) Mid-stream gravel bars in Denali National Park, Alaska. Image by Nic McPhee (https://www.flickr.com/photos/nicmcphee/214496166). Image licence: CC-BY-SA 2.0
- (centre) Image courtesy of Environmental Resource Management (ERM)
- (right) Secchi disc. Image by J. Albert Bowden II (https://www.flickr.com/photos/jalbertbowdenii/14878253738). Image licence: CC-BY 2.0

## Slide 2
Background & Introduction
Geotechnical engineers: engineering (e.g., bridges, anti-flood infrastructure) may impact flow
Hazard managers: flood hazard management
Environmental consultants: contamination from industrial sites within the catchment
Understanding multi-scale river processes is critical for many professionals
Upstream intervention can have significant impact downstream
Surveys require comparative data from sites along the watercourse.
Notes: Images:
- (left) Mid-stream gravel bars in Denali National Park, Alaska. Image by Nic McPhee (https://www.flickr.com/photos/nicmcphee/214496166). Image licence: CC-BY-SA 2.0
- (centre) Google Maps screen grab (Thames River, London)
- (right) Flood prevention barriers, Ireland, © Copyright Albert Bridge (http://www.geograph.ie/photo/5111498). Image licence: CC-BY-SA 2.0

## Slide 3
‘Real-world’ Examples
Professional river surveys often use stringent methodological protocols and expensive, high-tech equipment (e.g., remote sensing)
BUT
Many basic river analysis approaches available to GCSE and A Level students are the same or directly comparable to those used by ‘real-world’ practitioners
NASA/USGS airborne spectrometer for assessment of water quality (e.g., turbidity, phytoplankton volume, dissolved organic carbon content, suspended sediment volume)
e.g., USGS discharge survey from channel width, channel depth, flow velocity, wetted perimeter
USGS survey of sediment concentration by water sample drying and weighing
Online resources (e.g., Google Maps, national records)
Notes: Links to examples:
https://pubs.usgs.gov/wri/1998/4094/report.pdf
https://pubs.usgs.gov/sir/2013/5205/pdf/sir2013-5205.pdf
https://www.nasa.gov/feature/jpl/nasa-demonstrates-airborne-water-quality-sensor

## Slide 4
Pre-Fieldwork Activities
Research Questions & Hypotheses
For example:
Changes in river morphology associated with locations along a river course
Changes in river flow rate and bed-load/sediment carrying capacity along a river course
Impacts of human engineering and infrastructure on fluvial behaviour
Research should be framed around scientific questions & hypotheses
Notes: Images:
- (Top) Image modified from original by James St. John (https://www.flickr.com/photos/jsjgeology/39200485210). Image licence: CC-BY 2.0
- (Bottom) Permanent flow meter in Hampshire, UK, © Copyright Peter Facey (http://www.geograph.org.uk/photo/804111). Image licence: CC-BY-SA 2.0

## Slide 5
Direct access to a natural watercourse
Pre-Fieldwork Activities
Site Selection
River flowing across a floodplain
River flowing through an area of changing topography / gradient (e.g., steep river valley)
River meander site
River flowing through an urban area
River flow interrupted by full-width engineered structure (e.g., dam or weir)
River flow interrupted by other human intervention (e.g., bridge supports, flood defences)
Confluence of two watercourses
For comparison: man-made water course (i.e., a canal)
At least 2–3 sites for comparison
For example:

## Slide 6
Political & topographical maps (e.g., Ordnance Survey, Google)
National-, regional-, catchment-, local-scale
Geological maps (e.g., BGS iGeology App / BGS GeoIndex)
Satellite & aerial maps/images
Land use maps
Historical maps
e.g., Uppermill, Greater Manchester
Google Maps satellite image
1854 political map
Geological map
Pre-Fieldwork Activities
Metadata: Cartography
Notes: Images:
(left) Screen grab from Geological map from British Geological Survey Geology of Britain (http://mapapps.bgs.ac.uk/geologyofbritain3d/index.html)
(centre) Screen grab of historical (1854) map from https://www.old-maps.co.uk/#/Map/399649/405953/10/101748
(top right) Screen grab of Environment Agency flood risk map for Uppermill (https://flood-warning-information.service.gov.uk/long-term-flood-risk/map)

## Slide 7
Environmental Agency records
Hydrological data
Flood risk maps
Local and national press
e.g., National River Archives
(‘Tame at Uppermill’ gauging station)
Pre-Fieldwork Activities
Metadata: Other Secondary Data Sources
Notes: Images:
- Screen grabs from the National River Flow Archive (Tame at Uppermill gauging station; http://nrfa.ceh.ac.uk/data/station/info/69048)

## Slide 8
https://www.rgs.org/schools/teaching-resources/sampling-techniques/
Pre-Fieldwork Activities
Research Techniques
Dependent on field area/ field sites
Dependent on features & processes to measure
Dependent on research questions and hypotheses
Dependent on spatial and temporal scales of study
Dependent on available resources (i.e., time, money, expertise)
No ‘one size fits all’
Notes: Images:
(left) Silva Expedition 4 compass-clinometer (https://en.wikipedia.org/wiki/Silva_compass#/media/File:Silva_compass,_Expedition_4.jpg). Image licence: CC-BY-SA 3.0
(centre) Sonar depth measurement by (http://www.navy.mil/view_image.asp?id=2767). Image licence: Image in the Public Domain
(right) Using callipers to measure the a, b and c axes of a pebble by the Field Studies Council (https://www.geography-fieldwork.org/a-level/coasts/coastal-management/method/). Image licence: CC_BY

## Slide 9
Dependent on time available
Dependent on number of sites & transit times
Dependent on number of team members
Dependent on data collection techniques
Field Plan
Pre-Fieldwork Activities
Logistical Planning
Notes: Images:
- Pexels.com (stock photography with a CC0 licence)

## Slide 10
Clothing (long trousers, long sleeves, wet weather gear, boots)
Field note book
Charged mobile phone
GPS device
Camera
Sharpened pencils
First aid kit
Field Kit (Universal)
Field Kit (Fieldwork Specific)
Pre-Fieldwork Activities
Logistical Planning
Research equipment (e.g., metre ruler, callipers, etc.)
Notes: Images:
- Pexels.com (stock photography with a CC0 licence)

## Slide 11
Site Practicalities
Parking (incl. bus parking)
Toilets
Picnic sites
Shops & cafes
Field centres & visitor centres
Accessibility (roads, foot paths, etc.)
Nearest A&E Department
Pre-Fieldwork Activities
Logistical Planning
Notes: Images:
- Pexels.com (stock photography with a CC0 licence)

## Slide 12
Products of an evolving planet
Comparative Study of River Regimes Pre-Fieldwork Activities
Risk Assessment
https://www.rgs.org/in-the-field/fieldwork-in-schools/fieldwork-safety-and-planning/risk-assessments/
Working in/near water
Uneven / unstable ground
Biological hazards (insects, Giant Hogweed, etc.).
Hazard Control Measures Residual Risk
Assessment of flow conditions; work in groups, avoid loose clothing, always walk downstream, take small steps ……. etc.
Keep to flat areas; walk with care; ……. etc.
Insect repellent; stay away from undergrowth; ….. etc.
MEDIUM
LOW
LOW
Pre-Fieldwork Activities
Logistical Planning
Notes: Example of factors to consider (NOT exhaustive)

## Slide 13
https://www.rgs.org/schools/teaching-resources/a-student-guide-to-the-a-level-independent-investi/
https://www.rgs.org/schools/teaching-resources/rivers-(2)/
https://www.rgs.org/schools/teaching-resources/gcse-river-landscapes/
Pre-Fieldwork Activities
Logistical Planning
Other Resources
Notes: Image:
- Screen grab from RGS-IBG website (https://www.rgs.org/schools/teaching-resources/rivers-(2)/)

## Slide 14
Products of an evolving planet
Comparative Study of River Regimes Data Collection Technique
Data Collection Technique
Field Notebook
Critical fieldwork aspect
For professionals, field notebook can be a legal document
Record of sites, activities, & data
Date, time, weather conditions, investigator mood
Name of field site, GPS waypoint name, co-ordinates
Brief site description (e.g., land use, human infrastructure, natural features & processes, vegetation, other relevant observations)
River conditions (e.g., qualitative assessment of water level, flow rate, types of river bank, channelisation, etc.)
Site sketch
Record of methods & collected data
Where possible: catchment rainfall data from 1, 12, and 24 hours prior to site visit

## Slide 15
Products of an evolving planet
Comparative Study of River Regimes Data Collection Technique
Data Collection Technique
Field Notebook
Site Sketch Good Practice
Include major features
Sense of scale and spatial distribution of features
Notes: Images:
- (both) Images courtesy of Environmental Resource Management (ERM)

## Slide 16
Data Collection Technique
Morphology & Flow Regime: Introduction
Features that characterise the form and flow of a river
Cross-sectional area
Hydraulic radius
Wetted perimeter
Discharge
Gradient
River width
River depth
Flow velocity
Measured In Situ
Calculated From Field Data
Notes: Images:
- (top) Annotated Google Maps screen grab (Thames River, London)
- (bottom) Image courtesy of Environmental Resource Management (ERM)

## Slide 17
Products of an evolving planet
Data Collection Technique
Morphology & Flow Regime: Gradient
What is Measured?
Slope down which river is flowing
Controlling factor in river morphology and flow regime
Gradient = Δh /d
Difference in height between two sites divided by the distance between those sites
Place measuring poles a known distance apart (one upstream, one downstream with the direct line-of-sight perpendicular to flow)
Take angle between matching height horizons using a clinometer
Calculate gradient from equation:
Notes: Images:
(right) Measuring gradient Image by Olchfa-Geography (https://www.flickr.com/photos/olchfageography/828057367). Image licence: CC-BY-NC 2.0
(bottom left) Madcap, from Wikimedia Commons (https://commons.wikimedia.org/wiki/File:Grade_dimension.svg). Image licence: Image in the public domain.

## Slide 18
Data Collection Technique
Morphology & Flow Regime: Gradient
Site Requirements
Equipment & Costs
Data Resolution Needs
Ideal: direct access to river channel
Non-ideal (e.g., high flow conditions): access to riverbank
Surveying poles (moderate cost) or metre rulers (low cost)
Clinometer: home-made, smartphone app, plastic (all low cost)
Collect data for at least 3–5 locations across width of the river
Calculate an average (mean or median) value
Calculate data spread (e.g., standard deviation)
Notes: Images:
(top) Silva Expedition 4 compass-clinometer (https://en.wikipedia.org/wiki/Silva_compass#/media/File:Silva_compass,_Expedition_4.jpg). Image licence: CC-BY-SA 3.0
(bottom) Clinometer on a smartphone. Image by Rufiyaa (https://commons.wikimedia.org/wiki/File:Clinometer_on_smartphone.jpg). Image licence: CC-BY-SA 4.0

## Slide 19
Data Collection Technique
Morphology & Flow Regime: Gradient
Professional Measurement Techniques
Surveying poles & clinometers
Theodolites and laser-based equipment
LiDAR data
Digital Elevation Models (DEMs) derived from aerial & satellite images
Notes: Image:
- Theodolite surveying in Dublin, Ireland. Image by Kenneth Allen (http://www.geograph.ie/photo/4190504). Image licence: CC-BY-SA 2.0

## Slide 20
Products of an evolving planet
Data Collection Technique
Morphology & Flow Regime: River Width
What is Measured?
Distance across flowing water perpendicular to flow
and/or
Distance from one bank to the other (including areas of dry river bank and active flow)
Measured In Situ
Length of tape measure stretched one side to the other
Ideally, hold ~20 cm above water surface
Outer riverbanks = limits beyond which river would flood
Make note/measurements of gravel sections in channelised rivers
Measured Remotely
Rivers clearly visible from above can be measured from aerial or satellite images (e.g., Google Maps)
Caution: river width changes over multiple time scales (daily, seasonally, decadally, etc.)
Notes: Images:
Annotated Google Maps screen grab (Thames River, London)

## Slide 21
Data Collection Technique
Morphology & Flow Regime: River Width
Site Requirements
Equipment & Costs
Data Resolution Needs
Direct access to full width of river channel (in situ approach)
River clearly visible in aerial imagery (e.g., not obscured by vegetation, etc.; remote approach)
Tape measure (low cost; in situ approach)
Internet access (low cost; remote approach)
At least 5–10 measurements per site, taken at regular intervals along bank (e.g., 0.5– 1 m apart)
Calculate an average (mean or median) value
Calculate data spread (e.g., standard deviation)
Professional Measurement Techniques
Tape measure
Laser range finders
GPS mapping
Remote sensing (useful for studying temporal changes)

## Slide 22
Data Collection Technique
Morphology & Flow Regime: River Depth
What is Measured?
Vertical distance between the riverbed and surface
Measured using a metre ruler or surveying pole
Measurements taken from points along a transect perpendicular to flow
Data accuracy can be impacted by soft river bed (metre ruler sinks into sediment)
Make note of (and consider discarding) features that impact unusually on measurement (e.g., large boulders under metre ruler)
Notes: Images:
- (both) Images courtesy of Environmental Resource Management (ERM)

## Slide 23
Data Collection Technique
Morphology & Flow Regime: River Depth
Site Requirements
Equipment & Costs
Data Resolution Needs
Direct access to full width of river channel
Metre ruler (low cost) or surveying pole (moderate cost)
Depth should be measured at regular intervals across a transect perpendicular to flow
Intervals will depend on total river width and available time
For each point on the transect, measure at least 3–5 times
Calculate an average (mean or median) value
Calculate data spread (e.g., standard deviation)

## Slide 24
Data Collection Technique
Morphology & Flow Regime: River Depth
Professional Measurement Techniques
Surveying poles and metre rulers (shallow rivers)
Sonar sounding (deep and/or very wide rivers)
Notes: Images:
- (left) Brandon T. Fields (cdated) via the US Army Corps of Engineers - EM 1110-2-1003, Manual of Hydrographic Surveying, based upon Principle_of_SBES.jpg by en:User:Mredmayne.This W3C-unspecified vector image was created with Inkscape (https://commons.wikimedia.org/w/index.php?curid=23357601). Image licence: Image in the Public Domain
- (right) Sonar depth measurement by (http://www.navy.mil/view_image.asp?id=2767). Image licence: Image in the Public Domain

## Slide 25
Data Collection Technique
Morphology & Flow Regime: Flow Velocity
What is Measured?
Speed at which river water is flowing
Velocity = distance / time
Position two people at upstream and downstream locations, with a known distance between them (e.g., 5 m)
Upstream person drops a buoyant object into the river
Record the time taken for object to reach downstream person
Where river access not possible, less accurate measurement can be taken by dropping the item from bridge of known width and recording time taken to emerge from the other side
For best results, measure at different points across channel
Notes: Image:
- Measuring river flow velocity with rubber ducks. Gary Peeples, U.S. Fish and Wildlife Service Southeast Region. Image licence: CC BY 2.0 (https://creativecommons.org/licences/by/2.0), via Wikimedia Commons

## Slide 26
Data Collection Technique
Morphology & Flow Regime: Flow Velocity
Site Requirements
Equipment & Costs
Data Resolution Needs
Direct access to river channel where two individuals can stand in upstream and downstream positions ~ 5–10 m apart
Access to bridge spanning the river (non-ideal)
Brightly coloured, biodegradable object that floats but has sufficient weight to not be impacted by river waves or wind (e.g., an orange)
At least 5–10 repeat measurements
Consider measuring multiple points along transect perpendicular to flow (e.g., fast centre, slow along banks)
Calculate an average (mean or median) value
Calculate data spread (e.g., standard deviation)

## Slide 27
Data Collection Technique
Morphology & Flow Regime: Flow Velocity
Professional Measurement Techniques
Permanent flow meter stations
Handheld flow meters
Notes: Images:
- (right) Handheld water flow meter. By Wtshymanski. Image licence: CC-BY-SA 3.0 or GFDL (http://www.gnu.org/copyleft/fdl.html)], from Wikimedia Commons
- (left) Permanent flow meter in Hampshire, UK, © Copyright Peter Facey (http://www.geograph.org.uk/photo/804111). Image licence: CC-BY-SA 2.0

## Slide 28
Data Collection Technique
Morphology & Flow Regime: Calculations
Classroom–based Calculations
For calculation details, see Post-fieldwork Activities
Cross-sectional area
Hydraulic radius
Wetted perimeter
Discharge
Only wetted perimeter can be measured in situ (not recommended)
Wetted perimeter = part of channel bed in contact with water)
Cumbersome equipment needs (long, heavy chain)
Subject to river conditions (challenging in fast flowing water)
Difficult measurement technique (lay chain along riverbed, perpendicular to flow and confirming to riverbed morphology, then take total length)
Even in professional settings, usually estimated from calculation using other parameters

## Slide 29
Transportation capacity varies along a river’s course
Size and nature of materials being transported varies
Characterising river load allows estimates of energy within the system (e.g., larger pebbles demonstrate greater energy than do smaller pebbles)
Deposited materials record flooding history critical for hazard management
Water quality critical for water resource allocation and the environment
Data Collection Technique
Material Transport & Water Quality
Variables that demonstrate river’s ability to transport material downstream
Bed-load
Suspended sediments
Dissolved matter
Water quality
Variables that can be characterised

## Slide 30
Qualitatively assess sand grain size by comparison to a geological grain size chart
Quantitative assessment using grain sieves
Data Collection Technique
Transport of Solids: Bed-load
What is Measured?
Bed-load materials (gravel, pebbles, boulders, etc.) travel along the riverbed by the force of flowing water
Moves by bouncing and rolling
Reflects variations in river energy (e.g., upstream vs. downstream, outside of meander vs. inside of meander
Insights into both past and present flow conditions
Collect samples from regular intervals along a river-wide transect perpendicular to flow
To collect a sample, point finger and lower into water; collect the first pebble that it touches
Use callipers or a ruler to measure pebble axes
Record gravel bars (e.g., length, width, area, location in flow)
Notes: Images:
(top) Annotated river transport image. Image modified from: PSUEnviroDan. Image licence: Image in the Public Domain, via Wikimedia Commons
(bottom) Image modified from original by James St. John (https://www.flickr.com/photos/jsjgeology/39200485210). Image licence: CC-BY 2.0

## Slide 31
Data Collection Technique
Transport of Solids: Bed-load
Site Requirements
Equipment & Costs
Data Resolution Needs
Direct access to river channel
Plastic callipers or a ruler (low-cost)
Digital callipers (moderate to high cost)
Sediment sieves (moderate to high cost)
Geological grain size chart (low cost)
Take samples from multiple points across transect. Intervals depend on river width and time available
At each spot along transect, collect a single sediment sample or at least 10 pebbles
For pebbles, calculate average (mean or median) size
For pebbles, calculate data spread (e.g., standard deviation)
Notes: Images:
- Using callipers to measure the a, b and c axes of a pebble by the Field Studies Council (https://www.geography-fieldwork.org/a-level/coasts/coastal-management/method/). Image licence: CC_BY

## Slide 32
Data Collection Technique
Transport of Solids: Bed-load
Professional Measurement Techniques
Manual grain-size analysis (e.g., high-precision calliper measurements)
Laboratory-based testing of collected bed-load samples
Laboratory testing methods include:
Scanning electron microscopy (SEM; see images) for compositional and morphological analysis of bed-load material
Laser granulometry for grain size analysis
Notes: Image:
(top) Sand grains under SEM. Image courtesy of the Lewis Lab at Northeastern University (https://www.flickr.com/photos/adonofrio/albums/72157623620596451). Image created by Anthony D'Onofrio, William H. Fowle, Eric J. Stewart and Kim Lewis. Image licence: CC-BY 2.0
(bottom) Image by ZEISS Microscopy (https://www.flickr.com/photos/zeissmicro/10710025785). Image licence: CC-BY-SA 2.0

## Slide 33
Data Collection Technique
Transport of Solids: Suspended Sediments
What is Measured?
Materials suspended within the water and transported downstream
Too small to be sampled and measured by hand
Qualitatively and semi-quantitative assessment in situ
OR
Quantitative laboratory (or classroom) based techniques
In situ: Collect water sample in bottle, allow sediment to settle, note sediment layer thickness, colour, clarity of water
In situ: Lower Secchi disc into water and record depth at which it disappears
Laboratory: Collect sample of known volume, return to laboratory, allow to dry completely, weigh sediment residue
Notes: Images:
- Annotated river transport image. Image modified from: PSUEnviroDan. Image licence: Image in the Public Domain, via Wikimedia Commons

## Slide 34
Data Collection Technique
Transport of Solids: Suspended Sediments
Site Requirements
Equipment & Costs
Data Resolution Needs
Direct access to river channel
Suspended sediment load can vary across water flow; ideally, multiple samples should be taken across the river, along a transect perpendicular to flow
For Secchi disc measurements, repeat 5–10 times
2-L bottle for water collection (low cost)
Filter paper (low cost) and scales (low to high cost)
Ruler or tape measure (low cost)
Secchi disc (low [homemade] to moderate cost [purchased])
For Secchi disc measurements, calculate average (mean or median) depth of disappearance
For Secchi disc measurements, calculate data spread (e.g., standard deviation)
Notes: Image:
- Secchi disc. Image by J. Albert Bowden II (https://www.flickr.com/photos/jalbertbowdenii/14878253738). Image licence: CC-BY 2.0

## Slide 35
Data Collection Technique
Transport of Solids: Suspended Sediments
Professional Measurement Techniques
Secchi discs
Laboratory-based testing of collected water & sediment samples
Remote sensing techniques
Laboratory testing methods include:
Sample drying and weighing (using high precision scales)
Scanning electron microscopy (SEM) for compositional and morphological analysis of sediment grains
Laser granulometry for grain size analysis (see images)
Notes: Images:
- Mastersizer 3000 laser granulometer. By Plogeo. Image licence: CC BY-SA 4.0, from Wikimedia Commons

## Slide 36
Products of an evolving planet
Comparative Study of River Regimes Data Collection Technique
Data Collection Technique
Dissolved Matter & Water Quality
What is Measured?
Water quality analysis is critical for resource allocation and environmental protection
Colour & smell description (avoid tasting)
Turbidity (function of sediment load; see sediment load analysis for details)
Temperature (glass or digital thermometer)
pH (litmus paper or digital meter)
Basic Variables
Dissolved oxygen (digital dissolved oxygen meter or titration)
Total dissolved solids (digital meter)
Water conductivity (digital meter)
Dissolved nitrates and phosphates (digital spectrophotometer)
Invertebrate population (collected in net, compared to identification chart)
Carbon transport
Advanced Variables
Notes: Images:
(top left) Litmus paper by Chemicalinterest. Image licence: Image in the Public Domain, from Wikimedia Commons
(top right) Litmus colour chart pH scale. By Edward Stevens. Image licence: CC BY 3.0, from Wikimedia Commons
(bottom) Invertebrate sampling using a net and disturbing bottom sediments by kicking. Image © Copyright John Rostron (http://www.geograph.org.uk/photo/1430583). Image licence: CC-BY-SA 2.0

## Slide 37
Data Collection Technique
Dissolved Matter & Water Quality
Site Requirements
Equipment & Costs
Data Resolution Needs
Direct access to river channel
Litmus paper (low cost) or basic digital meters (temperature, pH; low to moderate cost)
Homemade Secchi disc (low cost) or purchased Secchi disc (moderate cost)
Plastic bottles for sampling (low cost)
Advanced digital meters (total dissolved solids, dissolved oxygen, conductivity, dissolved nitrate, dissolved phosphate; moderate to high cost )
Hach kits (all variables; moderate to high cost)
Sample nets, trays, biota identification charts (invertebrate sampling; low to moderate cost)
5–10 repeat analysis of each water sample
Calculate an average (mean or median) value
Calculate data spread (e.g., standard deviation)
Notes: Images:
(left) Digital pH meter. Ildar Sagdejev [GFDL (http://www.gnu.org/copyleft/fdl.html). Image licence: CC BY-SA 4.0, from Wikimedia Commons
(right) Hach kit. Science History Institute. Image licence: CC BY-SA 3.0, via Wikimedia Commons

## Slide 38
Data Collection Technique
Dissolved Matter & Water Quality
Professional Measurement Techniques
Portable digital meters (low cost and advanced versions)
Laboratory-based testing of collected water samples
Remote sensing techniques
Notes: Image:
- Digital pH meter. Ildar Sagdejev [GFDL (http://www.gnu.org/copyleft/fdl.html). Image licence: CC BY-SA 4.0, from Wikimedia Commons

## Slide 39
Post-Fieldwork Activities
Data Organisation & Input
For professionals, fieldwork is only the start
Post-fieldwork activities are the longest part of any project
Transfer field data to computer or tablet
Consider storage options (e.g., Microsoft Excel, ArcGIS, Google Earth)
For groups, develop data management plan & sharing facilities (e.g., Google Drive, Dropbox)
The first step is data organisation and management
Notes: Images:
(left) Microsoft excel screen grab
(right) Screen grab of Dropbox homepage (https://www.dropbox.com/?landing=dbv2)

## Slide 40
Post-Fieldwork Activities
Data Analysis & Interpretation
Appropriate use of:
Statistical techniques (e.g., data averaging, data spread, etc.)
Chart types and tables
Spatial analysis (e.g., ArcGIS, which is freely available to UK schools)
Data limitations should be considered and clearly presented
Interpretation and analysis should:
Reflect and be supported by the data
Compare and contrast different sites
Consider the results of similar studies & compare data with available secondary data sources
Return to original scientific questions and hypotheses
Consider how results would change under different conditions (e.g., changing seasons, after a storm event)
Consider how results may change in the future (e.g., impacts of climate change)

## Slide 41
Post-Fieldwork Activities
Data Analysis: Calculations
Cross-sectional Area & Discharge
Plot depth (y axis) as a function of distance across river (x axis)
Join the points to reveal cross-sectional shape of the riverbed
Contour string along length of the riverbed (or measure each segment using a ruler) and then measure the total length
Cross-sectional area (m2) = width (m) x mean depth (m)
Discharge (m3/s) = cross-sectional area (m2) x mean velocity (m/s)
Wetted Perimeter
Hydraulic Radius (i.e., Channel Efficiency)
Hydraulic radius (m) = cross-sectional area (m2) / wetted perimeter (m)
Reflects river’s ability to maintain energy whilst transporting material
Notes: Images:
- (both) Image courtesy of Environmental Resource Management (ERM)

## Slide 42
Use known depositional environment and pebble size to estimate flow velocity (and compare to values measured in the field)
Post-Fieldwork Activities
Data Analysis: Calculations
Pebble Size, Water Velocity and River Regime
Plot pebble size & river velocity on a Hjulström-Sundborg diagram (see right) to assess the river regime (i.e., erosion, transport, deposition)
Or
Or
For pebbles collected from dry river banks, calculate the river velocity when they were deposited by assuming a depositional environment
Notes: Image:
- Hjulströms_diagram, Karrockderivative work: Karrock (talk) (https://commons.wikimedia.org/w/index.php?curid=8258823). Image licence: CC BY-SA 3.0

## Slide 43
Post-Fieldwork Activities
Data Analysis: Calculations
Pebble Roundness
Cailleux roundness (R) = 2r x 1000 / L
L = average length of pebbles
r = average radius of curvature (obtained from a chart)
Use long and short axes measurements to perform particle shape analysis via pebble roundness indices (e.g., Cailleux Index)

## Slide 44
Post-Fieldwork Activities
Data Analysis: Calculations
Water Quality Assessment
Government guidelines
Past studies from the study area
Past studies from other study areas
Relevant secondary data sources
Compare measured data with:
For Example:
Compare Secchi disc data to those from the Secchi-Dip-In Project to assess relative levels of turbidity/suspended sediments
Use freshwater invertebrate data to calculate a Biological Monitoring Working Party (BMWP) score

## Slide 45
Products of an evolving planet
Comparative Study of River Regimes Post-Fieldwork Activities
Post-Fieldwork Activities
Data Reporting & Sharing
Data sharing & reporting must consider the needs of the audience
Can include written reports, oral presentations, graphical representations
Present at ‘conferences’, where different teams present concurrently using posters or talks
Data sharing and open access is required for some professionals
For others, data sharing is restricted to paid clients
Webpage creation
Social media & blogging
Citizen science platforms
To reach a broader audience:
Notes: Images:
- Pexels.com (stock photography with a CC0 licence)

## Slide 46
Village in the Saddleworth area of Oldham (Greater Manchester & South Pennines)
Case Study
Uppermill, Tame River Valley
Notes: Image:
- Google Maps screen grab (North West England)

## Slide 47
Confluence of the Tame and Diggle Brook (53°33'11.4"N 2°00'33.5"W)
Confluence of the Tame River and Diggle Brook
Free flowing river course
Gentle gravel riverbank
Adjoining land-use: grass and parkland
Case Study
Uppermill, Tame River Valley
Notes: Images:
- (all) Google Maps screen grabs (Confluence of the Tame and Diggle Brook at 53°33'11.4"N 2°00'33.5”W)

## Slide 48
Tame stepping-stones (53°32'54.6"N 2°00'28.0"W)
Stepping-stones across the Tame River
Stones (small-scale engineering) interrupt river flow
Access from Huddersfield Narrow Canal towpath
Access from public park in Uppermill Village
Case Study
Uppermill, Tame River Valley
Notes: Images:
- (all) Google Maps screen grabs (Tame stepping-stones at 53°32'54.6"N 2°00'28.0"W)

## Slide 49
Kitty’s Riverside Café Bar (53°32'50.7"N 2°00'23.5"W)
Busy urban road bridge
View down to the heavily engineered river course
River flow forced through confined space
Closer access to river below bridge
Case Study
Uppermill, Tame River Valley
Notes: Images:
- (all) Google Maps screen grabs (Kitty’s Riverside Café Bar at 53°32'50.7"N 2°00'23.5"W)

## Slide 50
Optional: Huddersfield Narrow Canal
Man-made watercourse
Controlled water flow
Case Study
Uppermill, Tame River Valley
Notes: Image:
- Huddersfield Narrow Canal. Image by David Dixon (http://www.geograph.org.uk/photo/2462856). Image licence: CC-BY-SA 2.0